## Slide 1
Nebula Topics
Astera Labs Proprietary & Confidential
Constraint Optimization through RTL Enhancement Using Generative AI
Problem Statement
Achieving timing closure is one of the biggest challenges in modern chip design. Engineers spend significant effort analyzing timing reports, identifying critical paths, and manually modifying RTL to meet performance targets — a time-consuming process requiring multiple design iterations. Opportunity to leverage Generative AI to analyze timing bottlenecks, recommend RTL optimizations, and accelerate timing closure while preserving functional correctness.
Objectives
Develop a GenAI-assisted framework to:
Analyze RTL designs against specified timing constraints
Identify critical paths and timing violations
Use GenAI to recommend RTL optimizations (pipelining, logic restructuring, retiming, FSM optimization)
Evaluate timing, area, and performance improvements
Formally verify equivalence between original and optimized RTL
RTL benchmark must include: 5 independent master async clock domains; ≥1 generated clock per master; Clock Domain Crossings (CDC); clock divider logic (multiple ratios); ~50K standard cells
Deliverables
RTL timing analysis framework
GenAI-based RTL optimization engine
Critical path and timing violation analysis
Optimized RTL implementation
Timing, frequency and PPA comparison
Formal equivalence verification report
Interactive demo showcasing RTL optimization workflow
Tools & Resources
Verilog/SystemVerilog
OpenSTA, Yosys, OpenROAD
SymbiYosys / EQY
Python
LLM/GenAI frameworks
AI/ML for Analog Circuit Design
Problem Statement
Demonstrate a fully automated framework for schematic design of analog circuits using Reinforcement Learning. Given circuit specifications, build an automated design flow that sizes devices using fewer search spaces (lowest design time) to reach near-optimal solutions. Use case: Equalizer circuit design (PCIe PHY). Should take significantly lower time than sweeping all MOS, R, C, L parameter space, with zero human intervention.
Specifications: Nyquist Freq (PCIe Gen 2, 5.0 Gbps): 2.5 GHz; HF peaking boost 3–12 dB (tunable 1.25–2.5 GHz); 1-Stage CTLE w/ source degeneration (variable Rs, Cs) + 1-Tap DFE; NRZ signaling; Linearity HD3 < -30 dB (100 MHz diff input); Input-referred noise < 1.5 mVrms (10 MHz–5 GHz); Power < 15 mW; Area < 0.05 mm² (130nm PDK); Eye opening > 0.4 UI (H) & > 100 mV (V); Meet across PVT (TT,SS,FF,SF,FS; VDD±5%; 0–125°C).
Objective
Develop a RL based automation framework to automatically design an equalizer for the given specifications, with minimal to zero human intervention
Deliverables
A Reinforcement Learning based Python framework that takes target specs as input, seamlessly integrates with a spice simulator — outputs the final schematic and resulting specs
Bonus: LLM-based human interaction with wrapper to fine-tune
Tools & Resources
Python, Anaconda
LLM, Gym Utils
Spice Simulators (NGSpice or PySpice)
Open-Source PDK (IHP 130nm BiCMOS or Skywater SKY 130nm)
CXL-Based Memory Optimization for MoE Models
Problem Statement
As AI models scale from dense Transformer architectures to MoE models, GPU memory capacity is becoming a key bottleneck. While HBM provides high bandwidth, its limited capacity restricts model scalability. CXL enables memory expansion, pooling, and disaggregation, offering a potential solution for next-generation AI systems.
Objectives
Study HBM and CXL memory architectures for AI inference
Analyze Transformer and MoE memory access patterns
Evaluate CXL-based memory expansion and pooling
Characterize bandwidth and latency trade-offs
Develop memory tiering strategies across HBM and CXL
Deliverables
HBM + CXL memory architecture model
CXL based Transformer & MoE workload analysis
Bandwidth, latency & scalability evaluation for CXL
Memory tiering and expert placement strategy
CXL memory expansion & pooling study
Simulation framework (HBM-only vs HBM+CXL)
Interactive demo/dashboard showcasing performance impact
Final report with architecture recommendations
Tools & Resources
Python, C/C++
gem5, SystemC, DRAMSim3
QEMU with CXL support
Open-source Transformer/MoE traces
Pandas, Matplotlib, Plotly
HBM and CXL specifications